## Slide 1: BSA CO-OP Muzzleloading Rifle Safety Briefing
NO PERCUSSION CAPS, BLACK POWDER, or BLACK POWDER SUBSTITUTE in the classroom NO EXCEPTIONS!

## Slide 2: Orientation Goal
To provide beginning shooters with the knowledge, skills, and attitude necessary to shoot a rifle safely under the direct supervision of a NRA Certified CO-OP ML Rifle Instructor or Certified NRA/NMLRA ML Instructor or a Certified NCS Shooting Sports Director.

## Slide 3: NRA Gun Safety Rules
ALWAYS keep your gun pointed in a safe direction
ALWAYS keep your finger off the trigger until ready to shoot
ALWAYS keep your gun unloaded until ready to use

## Slide 4: ML Rifle Parts…Percussion Cap Rifle
muzzle
rear sight
front sight
ramrod
barrel
butt plate
trigger
Three Major Parts: Lock, Stock, and Barrel
The Lock contains the hammer and the trigger
grip

## Slide 5: ML Rifle Parts…In-line Rifle
An Inline Rifle has the primer in the same line at the breech of the barrel
muzzle
grip

## Slide 6
Extend arms forward and form opening between the hands
With both eyes open, look at a distant object through opening
Bring hands to face while looking at object – Opening will be aligned with the dominant eye
Shooting Fundamentals Determining the Dominant Eye
Notes: 6

## Slide 7
Feet flat on the ground with the legs relaxed.
Seated directly behind the front support with slight lean forward.
Butt of the rifle in the shoulder close to neck.
Elbows on the table to support the rifle.
Support hand under the Forearm.
Trigger hand holding the grip.
Face firmly against the stock with eye looking straight down the sights.
Align the position to target.
Bench Rest Position
Notes: 7

## Slide 8
Seated on the ground with the legs crossed at ankles at 10-30 degrees to the target.
Seated directly behind the front support with slight lean forward.
Butt of the rifle in the shoulder close to neck.
Support hand holding the cross-sticks.
Trigger hand holding the grip.
Face firmly against the stock with eye looking straight down the sights.
Align the position to target.
Cross Stick Position
Notes: 8

## Slide 9: Rifle Shooting Fundamentals
1. AIMING (sight alignment & sight picture)
2. BREATH CONTROL
3. HOLD CONTROL
4. TRIGGER CONTROL
5. FOLLOW-THROUGH

## Slide 10: FUNDAMENTALS “Aiming”
Notch Rear and Post Front Sight
FRONT SIGHT IS IN SHARP FOCUS
Sight Alignment
  Sight Picture
  6 O'clock Hold on the Bullseye
With Post-and-Notch sights:
The tops of the front and rear sights are even
The front post is centered in the rear notch
Notes: 3 Min. Cumulative Time: 8 Min.
Instructor Notes: (Review Part I in Handbook)
NEW information: The bullseye has replaced the blank target and 6 O’clock hold on bullseye.
Ask What is a fundamental?
  Fundamentals are basic building blocks on which we can develop and expand.
Ask what is "Aiming?"
  Aiming is the process of positioning the rifle so that the bullet will hit the target.
  The process first involves sight alignment and then sight picture.
Ask What makes up sight alignment?
  The proper positioning of the shooting eye, rear sight and front sight.
Ask What makes up sight picture?
  The alignment of the shooting eye, rear sight, front sight and target or adding the target to aligned sights.
  The sight picture varies with the type of sights you are using, but the basic rule is to focus on the front sight (the rear sight and target will be slightly out of focus).
Explain 6 O’clock hold on the bullseye.
  Ball on a fence post. The ball is the bullseye and the post is the front sight.

## Slide 11: FUNDAMENTALS “Aiming”
Aperture Rear and Post Front Sight
FRONT SIGHT IS IN SHARP FOCUS
Sight Alignment
  Sight Picture
  6 O'clock Hold on the Bullseye
Aperture Rear and Post Front Sight
The top of the front sight is centered in the rear sight’s aperture
Notes: 3 Min. Cumulative Time: 8 Min.
Instructor Notes: (Review Part I in Handbook)
NEW information: The bullseye has replaced the blank target and 6 O’clock hold on bullseye.
Ask What is a fundamental?
  Fundamentals are basic building blocks on which we can develop and expand.
Ask what is "Aiming?"
  Aiming is the process of positioning the rifle so that the bullet will hit the target.
  The process first involves sight alignment and then sight picture.
Ask What makes up sight alignment?
  The proper positioning of the shooting eye, rear sight and front sight.
Ask What makes up sight picture?
  The alignment of the shooting eye, rear sight, front sight and target or adding the target to aligned sights.
  The sight picture varies with the type of sights you are using, but the basic rule is to focus on the front sight (the rear sight and target will be slightly out of focus).
Explain 6 O’clock hold on the bullseye.
  Ball on a fence post. The ball is the bullseye and the post is the front sight.

## Slide 12: Shooting Fundamentals Breath Control
Body movement while breathing can produce gun movement that impairs shooting accuracy.
  Pause breathing momentarily while firing the shot! (Respiratory pause)

## Slide 13: Shooting Fundamentals Hold Control
Body movement affects the shot.
  Hold your body still.
  Hold control involves you maintaining the proper sight picture and sight alignment during the process of firing the shot.

## Slide 14: Shooting Fundamentals Trigger Control
Trigger is pressed straight to the rear in a smooth, continuous manner without disturbing the sight picture.
Gradually and evenly increasing pressure until the mechanism releases.

## Slide 15: Shooting Fundamentals Follow-Through
In Rifle Shooting:
Follow through means to continue applying the other fundamentals before, during, and after the shot.
15

## Slide 16: Shooting Fundamentals The Fundamentals…A Review
“Maintaining sight alignment and acceptable sight picture.” –
“Pause breathing.” –
“Holding still.” –
“Moving only your trigger finger.” –
“To maintain position, and continue aiming, breath control, hold control, and trigger control until the gun settles back into the aiming area after the shot is fired.” –
AIMING
BREATH CONTROL
HOLD CONTROL
TRIGGER CONTROL
FOLLOW-THROUGH

## Slide 17: Most Important Fundamentals!
NOTE –
The TWO most IMPORTANT shooting fundamentals are……..
  “Maintaining sight alignment” – AIMING
  “Moving only the trigger finger” – TRIGGER CONTROL

## Slide 18: Accoutrements (Tools) needed to load a ML Rifle
18
powder flask
powder measure
short starter
patch and balls
ramrod
Capper & caps

## Slide 19: Determining if a Muzzleloader is loaded or unloaded
19
Instructor demonstration
  Position the gun – pointed in a safe direction
  Put ramrod into muzzle all the way to bottom of the barrel
  Mark rod at muzzle
  Pull rod out of barrel
  Place rod on side of barrel with mark aligned with the muzzle
  Look at the end of the rod to see how it aligns with the nipple.
    Unloaded: the end of the rod should be closely aligned with the nipple. Typically, within ½ inch.
    Loaded: The end the rod will be above the nipple typically by greater than an ½ inch.
The “sound check” is NOT acceptable for determining if a ML rifle is loaded.

## Slide 20: Pre-Preparation of a Muzzleloader for loading
20
Instructor demonstration DO NOT ACTUALLY LOAD
  Position rifle for loading – pointed in a safe direction
  Check bore for load
  Put hammer in half cock position & check nipple for a cap
  Swab barrel with wet patch
  Swab barrel with a dry patch
  Snap 3 caps to dry the flash channel
  Fill powder with the proper powder for the firearm
  Fill capper with caps

## Slide 21: Demonstrate Procedure for Loading a ML Rifle (use for every shot)
21
Instructor demonstration
DO NOT ACTUALLY LOAD
  “Smoke nipple” by pushing ramrod down the barrel and look for smoke coming out of the nipple to verify the rifle is clear to load. and/or dry fire with 1 cap to verify the barrel is clear.
  Fill powder measure from powder flask (maximum grains of powder not to exceed the caliber of the rifle. i.e. 50 grains for 50 caliber)
  Pour powder into muzzle
  Center patch over muzzle
  Place ball on patch over muzzle
  Use short starter “button” to start ball in muzzle (~1/2”)
  Tap ball into barrel with short rod of the starter (~6”)
  Use ramrod to drive the ball down. (Use short strokes so you don’t bend the rod.) Ball MUST Be Fully Seated on Top of Powder
  Once on the firing line, the instructor will place a cap on the nipple

## Slide 22: Supervision Requirements
NRA Certified Range Safety Officer
1 RSO per 8 participants 1:8 ratio
AND
NRA Certified CO-OP ML Rifle Instructor
OR
NRA/NMLRA Certified ML Instructor or Certified Shooting Sports Director.
1 Instructor per 1 participants 1:1 ratio

## Slide 23: Supervision Requirements
Loading and Firing MUST be supervised by the qualified instructor a 1 on 1 instructor to participant basis.
RSO ensures the safe operations according to range standard operating procedures. (SOP)
O

## Slide 24: Range Safety Briefing
NRA Safe Gun Handling Rules
ALWAYS keep your gun pointed in a safe direction.
ALWAYS keep your finger off the trigger until ready to shoot.
ALWAYS keep your gun unloaded until ready to use.

## Slide 25: Range Safety Briefing
Range layout
  Ready Area
  Firing Line
  Target Area
  Back Stop

## Slide 26: Range Safety Briefing
Other Safety Rules
  Know your target and what is beyond
  Wear eye and ear protection as appropriate
  Never use alcohol or drugs before or while shooting
  Be aware that certain types of guns and many shooting activities require additional safety precautions
Range Commands
  “Capping” (participant states just before snapping a cap)
  “Commence Firing”
  “Fire in the Hole” (participant states just before shot)
  “Cease Firing”

## Slide 27: Questions
What are your questions before you move to the Ready Area?