## Slide 1: BSA Rifle Range Safety Briefing
NO AMMUNITION in the classroom NO EXCEPTIONS!

## Slide 2: Orientation Goal
To provide beginning shooters with the knowledge, skills, and attitude necessary to shoot a rifle safely under the direct supervision of a NRA Certified Rifle Instructor or Certified NCS Shooting Sports Director.

## Slide 3: NRA Gun Safety Rules
ALWAYS keep your gun pointed in a safe direction
ALWAYS keep your finger off the trigger until ready to shoot
ALWAYS keep your gun unloaded until ready to use

## Slide 4: Rifle Parts…Air Rifle
Front Sight
Muzzle
Butt
Loading Port
Toe
Pellet Magazine
Trigger
Trigger Guard
Safety
Forearm
Barrel
Comb
Grip
Rear Sight
Chamber
Piercing Tube Cap

## Slide 5: Rifle Parts…Bolt Action
5
Grip
Butt
Toe
Comb
Chamber
Rear Sight
Barrel
Front Sight
Muzzle
Forearm
Box Magazine
Safety
Trigger Guard
Trigger
Bolt
Bolt Handle
Notes: 5

## Slide 6: Demonstrate Rifle Operation
Instructor demonstration only
  Loading with Dummy Ammo
  Cocking
  Firing “Dry-fire only” with Dummy Ammo
  Unloading
During Live-fire on the range, your instructor will load and unload the rifle for you.
6

## Slide 7
Extend arms forward and form opening between the hands
With both eyes open, look at a distant object through opening
Bring hands to face while looking at object – Opening will be aligned with the dominant eye
Shooting Fundamentals Determining the Dominant Eye
Notes: 7

## Slide 8: Rifle Shooting Fundamentals
1. AIMING (sight alignment & sight picture)
2. BREATH CONTROL
3. HOLD CONTROL
4. TRIGGER CONTROL
5. FOLLOW-THROUGH

## Slide 9
Feet flat on the ground with the legs relaxed.
Seated directly behind the front support with slight lean forward.
Butt of the rifle in the shoulder close to neck.
Elbows on the table to support the rifle.
Support hand under the Forearm.
Trigger hand.
Face firmly against the stock with eye looking straight down the sights.
Align the position to target.
Bench Rest Position
Notes: 9

## Slide 10
Prone Supported Position
Feet and legs are flat on the ground with the legs relaxed.
Butt of the rifle in the shoulder close to neck.
Elbows on the ground to support the rifle.
Support hand under the Forearm.
Trigger hand.
Face firmly against the stock with eye looking straight down the sights.
Align the position to target.
Notes: 10

## Slide 11: FUNDAMENTALS “Aiming”
Notch Rear and Post Front Sight
FRONT SIGHT IS IN SHARP FOCUS
Sight Alignment
  Sight Picture
  6 O'clock Hold on the Bullseye
With Post-and-Notch sights:
The tops of the front and rear sights are even
The front post is centered in the rear notch
Notes: 3 Min. Cumulative Time: 8 Min.
Instructor Notes: (Review Part I in Handbook)
NEW information: The bullseye has replaced the blank target and 6 O’clock hold on bullseye.
Ask What is a fundamental?
  Fundamentals are basic building blocks on which we can develop and expand.
Ask what is "Aiming?"
  Aiming is the process of positioning the rifle so that the bullet will hit the target.
  The process first involves sight alignment and then sight picture.
Ask What makes up sight alignment?
  The proper positioning of the shooting eye, rear sight and front sight.
Ask What makes up sight picture?
  The alignment of the shooting eye, rear sight, front sight and target or adding the target to aligned sights.
  The sight picture varies with the type of sights you are using, but the basic rule is to focus on the front sight (the rear sight and target will be slightly out of focus).
Explain 6 O’clock hold on the bullseye.
  Ball on a fence post. The ball is the bullseye and the post is the front sight.

## Slide 12: FUNDAMENTALS “Aiming”
Aperture Rear and Post Front Sight
FRONT SIGHT IS IN SHARP FOCUS
Sight Alignment
  Sight Picture
  6 O'clock Hold on the Bullseye
Aperture Rear and Post Front Sight
The tops of the front is center in the rear sights aperture
Notes: 3 Min. Cumulative Time: 8 Min.
Instructor Notes: (Review Part I in Handbook)
NEW information: The bullseye has replaced the blank target and 6 O’clock hold on bullseye.
Ask What is a fundamental?
  Fundamentals are basic building blocks on which we can develop and expand.
Ask what is "Aiming?"
  Aiming is the process of positioning the rifle so that the bullet will hit the target.
  The process first involves sight alignment and then sight picture.
Ask What makes up sight alignment?
  The proper positioning of the shooting eye, rear sight and front sight.
Ask What makes up sight picture?
  The alignment of the shooting eye, rear sight, front sight and target or adding the target to aligned sights.
  The sight picture varies with the type of sights you are using, but the basic rule is to focus on the front sight (the rear sight and target will be slightly out of focus).
Explain 6 O’clock hold on the bullseye.
  Ball on a fence post. The ball is the bullseye and the post is the front sight.

## Slide 13: FUNDAMENTALS “Aiming”
Aperture Rear and Aperture Front Sight
FRONT SIGHT IS IN SHARP FOCUS
Sight Alignment
  Sight Picture
  Bullseye is center in the front sight aperture
Aperture Rear and Post Front Sight
The front aperture is center in the rear sights aperture
Notes: 3 Min. Cumulative Time: 8 Min.
Instructor Notes: (Review Part I in Handbook)
NEW information: The bullseye has replaced the blank target and 6 O’clock hold on bullseye.
Ask What is a fundamental?
  Fundamentals are basic building blocks on which we can develop and expand.
Ask what is "Aiming?"
  Aiming is the process of positioning the rifle so that the bullet will hit the target.
  The process first involves sight alignment and then sight picture.
Ask What makes up sight alignment?
  The proper positioning of the shooting eye, rear sight and front sight.
Ask What makes up sight picture?
  The alignment of the shooting eye, rear sight, front sight and target or adding the target to aligned sights.
  The sight picture varies with the type of sights you are using, but the basic rule is to focus on the front sight (the rear sight and target will be slightly out of focus).
Explain 6 O’clock hold on the bullseye.
  Ball on a fence post. The ball is the bullseye and the post is the front sight.

## Slide 14: FUNDAMENTALS “Aiming”
Scope
FOCUS ON THE TARGET
Sight Alignment
  Sight Picture
  Cross Hairs are centered on the target
Looking through the scope , You see the whole scope tube (not just small hole in tube)
Notes: 3 Min. Cumulative Time: 8 Min.
Instructor Notes: (Review Part I in Handbook)
NEW information: The bullseye has replaced the blank target and 6 O’clock hold on bullseye.
Ask What is a fundamental?
  Fundamentals are basic building blocks on which we can develop and expand.
Ask what is "Aiming?"
  Aiming is the process of positioning the rifle so that the bullet will hit the target.
  The process first involves sight alignment and then sight picture.
Ask What makes up sight alignment?
  The proper positioning of the shooting eye, rear sight and front sight.
Ask What makes up sight picture?
  The alignment of the shooting eye, rear sight, front sight and target or adding the target to aligned sights.
  The sight picture varies with the type of sights you are using, but the basic rule is to focus on the front sight (the rear sight and target will be slightly out of focus).
Explain 6 O’clock hold on the bullseye.
  Ball on a fence post. The ball is the bullseye and the post is the front sight.

## Slide 15: Shooting Fundamentals Breath Control
Body movement while breathing can produce gun movement that impairs shooting.
  Stop breathing momentarily while firing the shot! (Respiratory pause)

## Slide 16: Shooting Fundamentals Hold Control
Body movement affects the shot.
  Hold your body still.
  Hold control allows you to maintain the proper sight picture and sight alignment during the process of firing the shot.

## Slide 17: Shooting Fundamentals Trigger Control
Trigger is pulled straight to the rear in a smooth, continuous manner without disturbing the sight alignment.
Gradually and evenly increasing pressure until the mechanism releases.
SURPRISE yourself when the gun shoots.

## Slide 18: Shooting Fundamentals Follow-Through
In Rifle Shooting:
Follow-through means to maintain aiming (perfect sight alignment and acceptable sight picture), breath control, hold control, and trigger control until the gun settles back into the aiming area after firing.
18

## Slide 19: Shooting Fundamentals The Fundamentals…A Review
“Maintaining perfect sight alignment and acceptable sight picture.” –
“Stop breathing.” –
“Holding still.” –
“Moving only your trigger finger.” –
“To maintain position, and continue aiming, breath control, hold control, and trigger control until the gun settles back into the aiming area after the shot is fired.” –
AIMING
BREATH CONTROL
HOLD CONTROL
TRIGGER CONTROL
FOLLOW-THROUGH

## Slide 20: Most Important Fundamentals!
NOTE –
The TWO most IMPORTANT shooting fundamentals are……..
  “Maintaining sight alignment” – AIMING
  “Moving only the trigger finger” – TRIGGER CONTROL

## Slide 21: Range Safety Briefing
Range layout
  Ready Area
  Firing Line
  Target Area
  Back Stop

## Slide 22: Range Safety Briefing
NRA Safe Gun Handling Rules
ALWAYS keep your gun pointed in a safe direction.
ALWAYS keep your finger off the trigger until ready to shoot.
ALWAYS keep your gun unloaded until ready to use.

## Slide 23: Range Safety Briefing
Other Safety Rules
  Know your target and what is beyond
  Wear eye and ear protection as appropriate
  Never use alcohol or drugs before or while shooting
  Be aware that certain types of guns and many shooting activities require additional safety precautions
Range Commands
  “Commence Firing”
  “Cease Firing”

## Slide 24: At The Firing Point
One instructor will be at each firing point.
The instructor will hold the rifle by the forearm.
Place your hands on the grip. When you have control of the rifle, say “Thank you” and the instructor will let go.
You will then Dry-fire. TAKE YOUR TIME. Focus on safety and the shooting fundamentals. When you are comfortable, tell the Instructor you are ready to shoot.
Your instructor will then load the rifle and hold it by forearm.
Place your hands on the grip. When you have control of the rifle, say “Thank you” and the instructor will let go.
You will Live-fire the prescribed number of shoots. Strive for consistent shot groups.

## Slide 25: Questions
Do you have any questions before you move to the Ready Area?